## Slide 1: Semi-Autonomous Parking System
EMBEDDED SYSTEMS DESIGN PROJECT
Under the guidance of : Prof. Dr. Mathias LINDEMANN
Keshav KUMAR, 33410
Keshavaditya GOLLA, 33392
Karan VERMA, 33398
Miaoshun WU, 33289
Shobhit GUPTA, 33435

## Slide 2: CONTENTS
Introduction
      Basic Flow of Events
Hardware Description
      Connecting to LEGO MINDSTORMS
Software description
      First Object Detection
      Parking Spot Detection
      Second Object Detection
      Parking Manoeuvre
      Stateflow
Conclusion

## Slide 3: INTRODUCTION
WHAT IS SAPS?
  Integrated Parking System in modern vehicles which increases comfort in parking in difficult parking environments.
  Velocity provided by driver as compared to Fully Autonomous Parking System.
  Sensors and Actuators scan environment for suitable parking spot.
  Parking Maneuver is performed if suitable spot without any obstacles is found.

## Slide 4: BASIC FLOW OF EVENTS IN SAPS

## Slide 5: HARDWARE DESCRIPTION
A typical LEGO MINDSTORMS EV3 set consists of:
• Programmable LEGO Brick
• Large Motor
• Medium Motor
• Ultrasonic Sensor
• Differential Gear
• Steering Mechanism
• Touch Sensor and more..

## Slide 6
HARDWARE DESCRIPTION
Programmable LEGO Brick:
Main processing centre which can be programmed as required
Can receive signals from up to four sensors using the input ports ( 1, 2, 3, 4)
Can controls up to 4 motors using the output ports ( A, B, C, D)

## Slide 7
Connecting to LEGO MINDSTORMS
The LEGO Brick can be connected to a PC/ Laptop in three modes:
1. Using USB Cable
2. Using Bluetooth
+
+
3. Using Wi-Fi

## Slide 8
HARDWARE DESCRIPTION
Large Motor: It provides the main drive to the bot.
Medium Motor: Control the steering of the bot.
Both motors have encoders built-in.
Ultrasonic Sensor: Measures distance between the sensor and object in front.
Touch Sensor: It’s an physical button used as a safety stop button

## Slide 9
HARDWARE DESCRIPTION
Simple Steering Mechanism: In this kind of steering, steering wheels are connected to each other and have individual pivot points.
Differential Gear Mechanism: While turning it allows the outer
drive wheel to rotate faster than the inner drive wheel thus decreasing the chances of slip.

## Slide 10: SOFTWARE DESCRIPTION
FIRST OBJECT DETECTION:
Ultrasonic Sensor Range should measure between 4cms and 20cms.
Object Length should be between 25 – 35cm.
Object Length (in cm ) = Encoder Value/9.9
If first object is a tree or group of trash cans , SAPS treats it as an invalid object.

## Slide 11
PARKING SPOT DETECTION:
Encoder is reset
Parking Length should be between 45 – 50 cm.
Ultrasonic Sensor should measure between 24 – 40 cm.
Parking Spot is rejected by SAPS if obstacle is present
SOFTWARE DESCRIPTION

## Slide 12
SECOND OBJECT DETECTION :
Encoder is reset again.
Object Length should be between 25 – 35 cm.
Ultrasonic sensor should measure between 4 – 20cm
After 2nd object is detected , SAPS performs parking maneuver.
SOFTWARE DESCRIPTION

## Slide 13: PARKING MANOEUVER:
After Parking Spot has been found.
Second object is found and confirmed with sufficient space.
Parking Manoeuvre is estimated, activated and then to be implemented.
  Constant Curvature Parking Manoeuvre:
  The path followed by the bot which is formed by joining arcs of two circles at one particular point.

## Slide 14: Constant Curvature Parking Manoeuvre
Parking Manoeuvre
(Curve ‘SC’)
Arc of Radius ‘R’
Parking spot
Vehicle
Object 1
Object 2

## Slide 15: Constant Curvature Parking Manoeuvre
For manoeuvring over the curve “SC”, using basic trigonometric functions :
From the ultrasonic sensor reading (Ds) we get the value of “D”.
  D = Ds + W/2
We have to calculate
N

## Slide 16: Constant Curvature Parking Manoeuvre
For different values of “D”, there are different starting points “S”
Once, starting point is determined we can determine the point “B”

## Slide 17: Constant Curvature Parking Manoeuvre
Now, Arc
At point S, Parking manoeuver starts
At point B, change in direction of steering wheels takes place
At point C, Parking manoeuver ends

## Slide 18: SOFTWARE DESCRIPTION
Stateflow

## Slide 19: SOFTWARE DESCRIPTION
Stateflow
State 1
State 2
event_or_message [condition]{condition_action}/transition_action

## Slide 20: SOFTWARE DESCRIPTION
Stateflow
State 1
State 2
Encoder reset
Encoder reset
State_nr=1
State_nr=2

## Slide 21: SOFTWARE DESCRIPTION
Stateflow